## Slide 1: Chapter 2
Point-to-Point Protocol (PPP)
Part II

## Slide 2: Point-to-Point Protocol (PPP)
PPP Concepts

## Slide 3: Introducing PPP
What is PPP?
  Recall that HDLC is the default serial encapsulation method when you connect two Cisco routers.
  Cisco HDLC can only work with other Cisco devices.
  When you need to connect to a non-Cisco router, you should use PPP encapsulation.
    PPP includes many features not available in HDLC.
    The link quality management feature monitors the quality of the link. If too many errors are detected, PPP takes the link down.
    PPP supports PAP and CHAP authentication.

## Slide 4: Introducing PPP
What is PPP?
  Three main components:
  HDLC:
    HDLC protocol for encapsulating datagrams over point-to-point links.
  LCP:
    Extensible Link Control Protocol (LCP) to establish, configure, and test the data link connection.
  NCPs:
    Family of Network Control Protocols (NCPs) for establishing and configuring different network layer protocols.

## Slide 5: Introducing PPP
What is PPP?
  Three main components:
  HDLC:
    HDLC protocol for encapsulating datagrams over point-to-point links.
  LCP:
    Extensible Link Control Protocol (LCP) to establish, configure, and test the data link connection.
  NCPs:
    Family of Network Control Protocols (NCPs) for establishing and configuring different network layer protocols.

## Slide 6: PPP Layered Architecture
PPP is a Data Link Layer protocol that provides a standard method for transporting multiprotocol datagrams over point-to-point links.
Translation: IP and IPX and others, simultaneously, over a single dialup or higher speed WAN link.
Synchronous or Asynchronous Physical Medium
Physical Layer
Network Control Protocol (NCP)
Data Link Layer
Network Layer
IP
IPX
Many Others
Link Control Protocol (LCP)
Point-to-Point Protocol (PPP)

## Slide 7: PPP Layered Architecture
PPP has a layered architecture:
  Link Control Protocol (LCP): To establish, configure and test the connection.
  Network Control Protocols (NCPs): A family of protocols to establish and configure Network Layer protocols.
Synchronous or Asynchronous Physical Medium
Physical Layer
Network Control Protocols (NCPs)
Data Link Layer
Network Layer
IP
IPX
Many Others
Link Control Protocol (LCP)

## Slide 8: PPP Layered Architecture
PPP can be configured on multiple types of interfaces:
  Asynchronous serial
  Synchronous serial
  High-Speed Serial Interface (HSSI)
  Integrated Services Digital Network (ISDN)
Network Control Protocols (NCPs)
Data Link Layer
Network Layer
IP
IPX
Many Others
Link Control Protocol (LCP)
Synchronous or Asynchronous Physical Medium
Physical Layer

## Slide 9: PPP Layered Architecture
PPP uses the Link Control Protocol (LCP) to negotiate and setup control options on the WAN link.
  Authentication, Compression, Error Detection, Multilink for load balancing, PPP Callback and link monitoring functions.
Synchronous or Asynchronous Physical Medium
Physical Layer
Network Control Protocols (NCPs)
Data Link Layer
Network Layer
IP
IPX
Many Others
Link Control Protocol (LCP)

## Slide 10: PPP Layered Architecture
Link Control Protocol (LCP)
Network Layer
IP
IPX
Many Others
PPP uses the Network Control Protocols (NCPs) to permit multiple network layer protocols to operate on the same communications link.
Synchronous or Asynchronous Physical Medium
Physical Layer
Network Control Protocols (NCPs)
Data Link Layer

## Slide 11: PPP Layered Architecture
Link Control Protocol (LCP)
Network Layer
IP
IPX
Many Others
For every network layer protocol used, a separate Network Control Protocol (NCP) is provided.
  NCPs include functional fields containing standardized codes to indicate the network layer protocol type that PPP encapsulates.
Synchronous or Asynchronous Physical Medium
Physical Layer
Data Link Layer
IPCP
IPXCP
Many Others

## Slide 12: FYI - PPP Protocol Suite
Data Link
Physical
Application
Presentation
Session
Transport
Network
PPP
LAN / WAN
Multiple Network Protocols
BAP, CHAP, EAP, LCP, LEX, LQR, PAP
ATCP ECP NBFCP BCP IPCP OSINLCP BACP IPv6CP SDCP CCP IPXCP SNACP DNCP LEXCP
PPP-BPDU
MLP
PPPoE
Control Protocols
Link Protocols
Multilink
Remote Bridges
PPP Over Ethernet

## Slide 13: FYI - PPP Protocol Suite
PPP-BPDU: PPP Bridge Protocol Data Unit
MLP: Multilink PPP
PPPoE: PPP Over Ethernet
Link Protocols:
  BAP: Bandwidth Allocation Protocol
  CHAP: Challenge Handshake Authentication Protocol
  EAP: Extensible Authentication Protocol
  LCP: Link Control Protocol
  LEX: LAN Extension Interface Protocol
  LQR: Link Quality Report
  PAP: Password Authentication Protocol

## Slide 14: FYI - PPP Protocol Suite
Control Protocols:
  ATCP: AppleTalk Control Protocol
  BACP: Bandwidth Allocation Control Protocol
  BCP: Bridging Control Protocol
  CCP: Compression Control Protocol
  DNCP: DECNet Phase IV Control Protocol
  ECP: Encryption Control Protocol
  IPCP: IP Control Protocol
  IPv6CP: IPv6 Control Protocol
  IPXCP: Novell IPX Control Protocol
  LEXCP: LAN Extension Interface Control Protocol

## Slide 15: FYI - PPP Protocol Suite
Control Protocols:
  NBFCP: NETBIOS Frames Control Protocol
  OSINLCP: OSI Network Layer Control Protocol
  SDCP: Serial Data Control Protocol
  SNACP: Systems Network Architecture Control Protocol

## Slide 16: PPP Frame Structure
Notice how the PPP frame has been modeled very closely on the standard HDLC frame.
The protocol field contains specific codes.

## Slide 17: FYI - PPP Frame Structure
The protocol code determines what protocol in the suite receives the payload.
Protocol Field Range (Hex)
Description
02xx – 1Exx xx01 – xx1F
Not Used (compression inefficient)
0xxx – 3xxx
Datagram belongs to a specific network protocol
8xxx – Bxxx
Datagram belongs to an associated NCP
4xxx – 7xxx
Datagram belongs to a low-volume protocol with no NCP
Cxxx - Exxx
Datagram is a control protocol

## Slide 18: FYI - PPP Frame Structure
Some of those codes:

## Slide 19: Establishing a PPP Session
PPP session establishment progresses through Three Phases.

## Slide 20: Establishing a PPP Session
Phase 1 – Link Establishment:
  The LCP must first open the connection and negotiate configuration options.
Phase 2 – Determine Link Quality (Optional):
  The LCP tests the link to determine whether the link quality is sufficient to bring up network layer protocols.
Phase 3 – Network Protocol Negotiation:
  The appropriate NCP separately configures the network layer protocols.
  The NCP can bring them up and take them down at any time.

## Slide 21: Establishing a Link with LCP
Phase 1 – Link Establishment:
  In this phase each PPP device sends LCP frames to configure and test the data link.
  LCP frames contain a configuration option field that allows devices to negotiate the use of options such as:
    The maximum transmission unit (MTU)
    Compression of certain PPP fields
    The link-authentication protocol.

## Slide 22: Establishing a Link with LCP
If a configuration option is not included in an LCP packet, the default value is assumed.
Before any network layer packets can be exchanged, LCP must first open the connection and negotiate the configuration parameters.
This phase is complete when a configuration acknowledgment frame has been sent and received.

## Slide 23: Establishing a Link with LCP
Authentication:
  After the link has been established and the authentication protocol decided on, the peer may be authenticated.
  Authentication, if used, takes place before the network layer protocol phase is entered.

## Slide 24: Establishing a Link with LCP
As part of this phase, LCP also allows for an optional link-quality determination test.
  The link is tested to determine whether the link quality is good enough to bring up network layer protocols.

## Slide 25: Network Layer Protocol Negotiation
PPP permits multiple Network layer protocols to operate on the same communications link.
  For every Network layer protocol used, PPP uses a separate NCP module.
    IP uses the IPCP module.
    IP Version 6 uses the IPv6CP module.
    IPX uses the IPXCP module.

## Slide 26: Network Layer Protocol Negotiation
In this phase the PPP devices send NCP packets to choose and configure one or more network layer protocols (e.g. IP).
Once each of the chosen network layer protocols has been configured, packets from each network layer protocol can be sent over the link.
If LCP closes the link, it informs the network layer protocols so that they can take appropriate action.

## Slide 27: Network Layer Protocol Negotiation
The show interfaces command reveals the LCP and NCP states under PPP configuration.
NCPs
LCP open = connection made.

## Slide 28: FYI - PPP Configuration Options

## Slide 29: PPP Configuration Commands
Enabling PPP:
  Router#config t
  Router(config)#interface s0/2/0
  Router(config-if)#encapsulation ppp
Configuring Compression:
  You can configure point-to-point compression on serial interfaces after you have enabled PPP. Because this option invokes a software compression process, it can affect system performance. If the traffic already consists of compressed files (.zip, .tar, or .mpeg, for example), do not use this option.
  Router(config-if)#compress [predictor|stac]

## Slide 30: PPP Configuration Commands
Link Quality Monitoring:
  LCP provides an optional link quality determination during the LCP Negotiation.
  If the link quality percentage is not maintained, the link is deemed to be of poor quality and is taken down.
  Router(config-if)#ppp quality percentage
Load Balancing Across Links:
  Multilink PPP (also referred to as MP, MPPP, MLP, or Multilink) provides a method for spreading traffic across multiple physical WAN links.
  Router(config-if)#ppp multilink

## Slide 31: Verifying a Serial PPP Configuration
Use the show interfaces serial command to verify proper configuration PPP encapsulation.
  When you configure PPP, the output of the show interfaces serial command should show "encapsulation ppp".
  When you configure PPP, you can check its LCP and NCP states.

## Slide 32: Troubleshooting PPP Encapsulation

## Slide 33: Point-to-Point Protocol (PPP)
PPP Authentication

## Slide 34: PPP Authentication Protocol - PAP
Password Authentication Protocol (PAP):
  Not a strong protocol.
  Username/Password sent in clear text.
  Uses a two-way handshake.
  Remote node in control of attempts.
    Username/Password pair are repeatedly sent across the link until authentication is acknowledged or the link is terminated.

## Slide 35: Configuring PAP
Rtr(config)#username remote-host password remote-password
This needs to match the ppp pap sent-username and password on the remote host.
When received and validated, routers with these username/password combinations will be allowed to connect.
Rtr(config-if)#ppp pap sent-username local-host-username password local-host-password
The passwords do not have to be the same on the remote and the local routers.
It should not be the same as the enable-secret password.

## Slide 36
hostname SantaCruz
username HQ password HQpass
interface serial 0/2/0
ip address 172.25.3.5 255.255.255.252
encapsulation ppp
ppp authentication pap
ppp pap sent-username SantaCruz password SantaCruzpass
hostname HQ
username SantaCruz password SantaCruzpass
interface serial 0/2/0
ip address 172.25.3.6 255.255.255.252
encapsulation ppp
ppp authentication pap
ppp pap sent-username HQ password HQpass
PAP
Remote usernames and passwords
Local usernames and passwords

## Slide 37
1
1. Establish PPP Link
2
2. Configuration request for PAP authentication.
3
3. Configuration ACK.
4
4. SantaCruz sends the SantaCruz username and SantCruzpass password configured for the interface.
5. HQ looks up the received name, retrieves the password and compares configured to received.
5
6. If they are the same, send an ACK and allow access. If they are not the same, send a NACK and terminate the connection.
6
ACK
NACK

## Slide 38: PPP Authentication Protocol - CHAP
Challenge Handshake Authentication Protocol (CHAP):
  The preferred authentication protocol.
  Uses a three-way handshake.
  Challenge/Response messages use MD5 hashing on random values and the password.
  Challenge/Response sequence repeated at random periods during the connect.

## Slide 39: PPP Authentication Protocol - CHAP
CHAP provides protection against playback attack through the use of a variable and hashed challenge value that is unique and unpredictable.
The use of repeated challenges is intended to limit the time of exposure to any single attack.
Unlike PAP, the local router or a third-party authentication server is in control of the frequency and timing of the challenges.

## Slide 40: PPP Authentication – CHAP Challenge
A CHAP challenge packet is built by the HQ router with the following characteristics:
  01 = challenge packet type identifier.
  ID = sequential number that identifies the challenge.
  random = a reasonably random number generated by the router.
  HQ = the authentication name of the challenger.
SantaCruz calls HQ and establishes a ppp link.

## Slide 41: CHAP Challenge
The ID and random values are kept on the HQ router or the called router.
The challenge packet is sent to the calling router.
A list of outstanding challenges is maintained.

## Slide 42: CHAP Challenge
The name HQ is used to look up the password.
Receive CHAP Challenge
The ID value, the random value and the password are fed into the MD5 hash generator.
The result is the one-way MD5-hashed CHAP challenge that will be sent back in the CHAP response.

## Slide 43: CHAP Challenge
The response packet is assembled and sent.
  02 = CHAP response packet type identifier.
  ID = copied from the challenge packet.
  hash = the output from the MD5 hash generator.
  SantaCruz = the hostname of the responding device. (From the hostname command or the ppp chap hostname command).
CHAP Response

## Slide 44: CHAP Challenge
The ID is used to find the original challenge packet.
Receive CHAP Response
The name is used to look up the password from a configured name or a security server.
The original ID, the original random value and the password are fed into the MD5 hash generator.

## Slide 45: CHAP Challenge
The hash value received in the response packet is then compared to the calculated MD5 hash value.
CHAP authentication succeeds if the calculated and the received hash values are equal.
Receive CHAP Response

## Slide 46: CHAP Challenge
If authentication is successful, a CHAP success packet is built from the following components:
  03 = CHAP success message type.
  ID = copied from the response packet.
  “Welcome In” is simply a text message providing a user-readable explanation.
Success OR Failure
03
Welcome In

## Slide 47: CHAP Challenge
If authentication fails, a CHAP failure packet is built from the following components:
  04 = CHAP failure message type.
  ID = copied from the response packet.
  “Authentication failure” or other text message, providing a user-readable explanation.
Success OR Failure
03
Welcome In
03
Welcome In
04
Authentication Failed

## Slide 48: PPP Configuration Command Summary
Router(config)#username name password password
Router(config)#interface serial 0/2/0
Router(config-if)#ip address address subnetmask
Router(config-if)#encapsulation ppp
Router(config-if)#ppp authentication chap
OR
Router(config-if)#ppp authentication pap
Router(config-if)#ppp pap sent-username name password password

## Slide 49: debug ppp Command Summary
debug ppp argument
  debug ppp authentication
      Display the authentication exchange sequence.
  debug ppp chap
      Display CHAP packet exchanges.
  debug ppp error
      Display protocol errors and error statistics.
  debug ppp negotiation
      Display packets during connection establishment.
  debug ppp packet
      Display packets being sent and received.